Ball Handling with Various Steering Systems
Leif Bennett, Mentor, Team 1515

Because the ball can't be drawn far under the robot's frame perimeter, crab drive may make it easier to turn with the ball.

The difficulty in handling the ball using ordinary steering systems is that the ball is very near one edge of the robot (which I'll call the front for convenience; the same considerations apply for other edges). If the robot pivots about its center axis, as in a tank drive's neutral turn, or about its rear axle, as with a conventional auto's steerable front wheels, the front edge will move sideways out from behind the ball.

Tank Drive Neutral Turn	Front Wheel Steering

On the other hand, a crab drive robot (all wheels powered and steerable, or Meccanum wheels, or other steering systems with X, Y, and yaw degrees of freedom), or one with steerable back wheels, would be able to turn with the front edge making little or no sideways movement. I don't know if crab drive will do well on the ramps.
However, standard tank steering (where each side's wheels or tracks can drive forwards or backwards independently, but cannot change angle with respect to the robot body, giving only two degrees of freedom) gives the possibility of a pinned turn, in which one side stops and the other side moves forwards. While the front moves sideways similarly to a neutral turn, it will also be moving forwards, which will at least tend to keep some contact with the ball. We may find it sufficient to have the drivers understand that a pinned turn is better than a neutral turn for ball handling.
Crab Drive Forward Turn	Tank Drive Neutral Turn
or Rear Wheel Steering